## Slide 1
DRDL AEROSPACE AI PLATFORM
ML-Driven Aerodynamic Prediction
& Design Optimization
A surrogate-model + evolutionary-optimization system replacing
CFD simulation with instant, data-driven aerodynamic analysis.
XGBOOST • DIFFERENTIAL EVOLUTION • FLIGHT ENVELOPE ANALYSIS

## Slide 2
WHAT IT IS
An Intelligent Replacement for Traditional CFD Workflows
The DRDL Aerospace AI Platform is a desktop application that predicts and optimizes the aerodynamic performance of an aircraft configuration in real time. Instead of running slow, resource-intensive CFD simulations for every design change, the platform uses a machine-learned surrogate model trained on prior simulation data to deliver instant aerodynamic estimates — enabling rapid design iteration and exploration.
P
Prediction Engine
Takes 18 geometry & flight-condition parameters and instantly returns CL, CD, XCP and CL/CD.
O
Design Optimizer
Searches the parameter space to find the geometry that best maximizes aerodynamic efficiency.
E
Flight Envelope Analysis
Sweeps angle of attack, Mach number, and altitude to characterize performance across conditions.
DRDL AEROSPACE AI PLATFORM
2

## Slide 3
METHODOLOGY
Two Core Techniques Power the Platform
ML
XGBoost Prediction Model
Supervised regression surrogate
Trained on prior aerodynamic simulation data (CL, CD, XCP as targets)
18 input features covering nose, wing, tail geometry and flight conditions (Mach, alpha, altitude)
Inputs normalized with a MinMaxScaler before inference
Loaded once from serialized .pkl model files — no live CFD or dataset access at runtime
Feature-importance ranking identifies the 5 most influential design parameters
DE
Differential Evolution Optimizer
Population-based evolutionary search
Custom DE loop searches the top 5 most influential parameters within user-defined bounds
Fitness function balances lift-to-drag ratio (95% weight) with proximity to a target center of pressure (5% weight)
Hard constraint rejects candidates with unrealistically low drag
Evaluated directly against the XGBoost model — no simulation required per generation
Tracks a Top-5 heap of best unique solutions across all generations
DRDL AEROSPACE AI PLATFORM
3

## Slide 4
HOW IT WORKS
From Design Parameters to Optimized Configuration
1
Input Parameters
18 geometry &
flight-condition values
→
2
Scaling
MinMax normalization
of input features
→
3
XGBoost Model
Predicts CL, CD, XCP
from scaled inputs
→
4
Outputs
CL / CD / XCP / CL-CD
+ accuracy metrics
DE
Optimization Loop (Tab 2)
The DE optimizer repeatedly proposes candidate parameter sets for the 5 most influential variables, evaluates each one through the same XGBoost model (step 3 above), and scores it using the lift-to-drag / center-of-pressure fitness function. Across generations the population evolves toward better solutions; the best design and its Top-5 alternatives are returned once the run completes.
DRDL AEROSPACE AI PLATFORM
4

## Slide 5
OUTPUTS & RESULTS
What the Platform Delivers
CL
Lift Coefficient
CD
Drag Coefficient
XCP
Center of Pressure
CL/CD
Aerodynamic Efficiency
Optimization Results
Best-performing geometry and its predicted CL, CD, XCP, CL/CD
Top-5 ranked alternative configurations with fitness scores
Fitness evolution, metrics-per-generation, and CL/CD vs. XCP plots
Exportable artefacts: best_geometry.csv, full_performance.csv, evolution history
Flight Envelope Results
Alpha sweep: CL, CD, XCP vs. angle of attack
Mach sweep: CL, CD, CL/CD vs. Mach number
Altitude sweep: CL, CD, CL/CD vs. altitude
Summary statistics table + all plots auto-saved as PNG
DRDL AEROSPACE AI PLATFORM
5

## Slide 6
KEY TAKEAWAYS
Faster Design,
Smarter Decisions
1
Replaces slow CFD runs with an instant, trained XGBoost surrogate model for CL, CD and XCP prediction.
2
Differential Evolution automatically discovers high-performance geometries under real design constraints.
3
Flight Envelope analysis validates performance across the full range of angle of attack, Mach, and altitude.
4
A single interactive GUI unifies prediction, optimization, and envelope analysis with real-time visualization and exportable results.
DRDL AEROSPACE AI PLATFORM
6