## Slide 1
DRDL — CARS PROJECT
Optimal Aerodynamic Configuration
Design of Aerospace Vehicles
A Data-Driven Framework using XGBoost Surrogate Modelling
and Differential Evolution Optimization
Submitted by: Veldi Sai Krishna, B.Tech CSE (AI & ML) Guru Nanak Institutions Technical Campus, Hyderabad Mentor: Kalidasu, Scientist 'E', DRDL Duration: 1 Sept 2025 – 27 Feb 2026

## Slide 2
Overview, Problem Statement & Objectives
OVERVIEW
DRDL initiated the CARS project to explore Data Science for the design of a complex "missile-like" aerospace vehicle (nose, wing, body, tail). A baseline configuration is refined using a fusion of theory, CFD/experimental data and machine learning to reach an optimal aerodynamic design.
PROBLEM STATEMENT
Conventional aerodynamic design relies on repeated, computationally expensive CFD simulations and experimental iterations, which are slow and often converge to a sub-optimal configuration. A methodology is needed that can predict aerodynamic performance rapidly and search the full design space — across the entire flight envelope — for a truly optimal, physically valid geometry.
Source: Aero Documentation, Sec. 1–2 | Internship Report — Project Abstract
PROJECT OBJECTIVES
a
Develop a prediction methodology for aerodynamic parameters using Machine Learning / Deep Learning
b
Validate the ML-based prediction methodology against existing CFD / experimental results
c
Perform shape optimization of the vehicle configuration at a fixed flight condition
d
Validate the code / methodology for an unknown vehicle configuration
e
Complete documentation of methodology, tools and results
Optimal Aerodynamic Configuration Design of Aerospace Vehicles
2

## Slide 3
Methodology: Surrogate Modelling + Evolutionary Optimization
SYSTEM ARCHITECTURE
Aerodynamic Data Generation
(Datcom / CFD / Empirical — 15 geometry vars, Mach 0.2–0.8, α 0–20°, Alt 0 & 6 km)
Dataset (~10,000 samples): Geometry + Flight Conditions → CL, CD, XCP
XGBoost Surrogate Models (fitness function)
predict CL, CD, XCP | extensions: MLP (CN, CM), Ensemble-XGBoost
Differential Evolution Optimizer
(mutation, variable crossover, Maximum Crossover, selection)
Optimal Aerodynamic Configuration
(validated across full flight envelope)
OPTIMIZATION FLOWCHART (per Fig. 13)
1
Inputs: baseline geometry, flight conditions, priority weights
2
Generate initial population of candidate geometries
3
For each generation → for each candidate: generate mutant vector
4
Crossover → trial vector (variable Cr + Maximum Crossover)
5
Evaluate fitness: XGBoost predicts CL, CD, XCP over 110 flight points; weighted average → fitness
6
Selection: keep trial vector only if fitness improves & constraints met
7
Repeat until all candidates / generations traversed
8
Output: configuration with best fitness (optimal geometry)
Optimal Aerodynamic Configuration Design of Aerospace Vehicles
3

## Slide 4
Results & Discussion
Fig. 5 & 6 — XGBoost Predicted vs Actual CL (R² = 0.9994) and CD (R² = 0.9996)
Fig. 9 a & b — CL/CD vs α, Mach 0.8, Ground level (Uniform / Variable weights)
Fig. 11 — XCP Training (R² = 0.9998) vs Testing (R² = 0.9451) Data
Peak CL/CD improvement ≈ 67% (α = 3–8°) • Weight increase only ≈ 1.7% (Steel AISI 304) • CN = 0.54, CM/CD = 7.67 at optimal design points
Discussion: XGBoost reliably captured non-linear CL/CD/XCP behaviour across the flight envelope, replacing repeated CFD/Datcom runs. Differential Evolution, guided by this surrogate, converged to configurations with markedly better lift-to-drag ratio at negligible weight cost — validated by DRDL on Datcom re-runs of the modified geometry.
Source: exact result figures reproduced from the Aero Documentation (Figs. 5, 6, 9, 11)
Optimal Aerodynamic Configuration Design of Aerospace Vehicles
4

## Slide 5
Recommendations, Conclusion & Future Scope
RECOMMENDATIONS / SOLUTIONS
Use variable (non-uniform) flight-point weighting to prioritize critical Mach/alpha regions of the envelope
Adopt the Maximum Crossover enhancement — improves DE convergence by ~80% over classical DE
Apply hard/soft geometric and structural constraints (e.g., CD ≥ 0.12, tail/body sizing) during optimization
Validate any optimized geometry's structural weight impact before finalizing (as done for Steel AISI 304)
Extend surrogate ensembles (XGBoost + MLP) for additional coefficients such as CN and CM
CONCLUSION
All five project objectives were achieved. A complete methodology now exists for optimal aerodynamic design of a multi-component aerospace vehicle across its full flight envelope, with designer-set priority weights and constraints.
The XGBoost surrogate + Differential Evolution framework delivered configurations with significantly higher CL/CD, reduced drag, and stable behaviour, validated against Datcom re-runs — while cutting computation time versus repeated CFD/experimental analysis.
This confirms ML-driven surrogate modelling combined with evolutionary optimization as a reliable, efficient alternative to conventional simulation-based aerodynamic design.
FUTURE SCOPE
Multi-objective optimization to jointly maximize CN and CM/CD (currently solved independently)
Physics-Informed Machine Learning: merge Data Generation, Fitness Function and Evolutionary Design into one unified pipeline
Extend the framework to more complex, multi-component aerospace vehicle configurations
Broaden constraint handling to structural, stability and other engineering domains
Optimal Aerodynamic Configuration Design of Aerospace Vehicles
5