## Slide 1
PROJECT REPORT
Optimal Aerodynamic Configuration
Design of Aerospace Vehicles
A Data-Driven Framework using Machine Learning Surrogate Modelling
(XGBoost) and Differential Evolution Optimization
PRESENTED BY
Veldi Sai Krishna — B.Tech CSE (AI & ML)
INSTITUTION
Guru Nanak Institutions Technical Campus, Hyderabad
ORGANIZATION
Research Centre Imarat (RCI), DRDO | Mentor: Kalidasu, Scientist 'E'
DURATION
01 September 2025 – 27 February 2026

## Slide 2
2
Overview, Problem Statement & Objectives
OVERVIEW
The project develops a prediction methodology for aerodynamic parameters (CL, CD, XCP) using Machine Learning, validates it against CFD/experimental (Datcom) data, and uses it to shape-optimize an aerospace vehicle configuration — replacing repeated, costly simulation with a fast ML surrogate + optimizer.
PROBLEM STATEMENT
A typical aerodynamic configuration is arrived at through a fusion of empirical, numerical and experimental methods, plus experience from a baseline design — a process that is often sub-optimal. Data Science offers a way to instead pursue a truly optimal aerodynamic configuration design.
OBJECTIVES
1
Predict:
Predict — Develop a prediction methodology for aerodynamic parameters using ML / Deep Learning
2
Validate:
Validate — Validate the ML-based methodology against existing CFD / experimental results
3
Optimize:
Optimize — Shape-optimize the aerospace vehicle configuration at a fixed flight condition
4
Generalize:
Generalize — Validate the code / methodology for an unknown vehicle configuration
5
Document:
Document — Document methodology, tools and results (this deliverable)

## Slide 3
3
Methodology & System Architecture
Baseline “missile-like” configuration (Nose-Wing-Body-Tail), 15 geometry variables modulated → Datcom-generated data across 110 flight conditions (Mach 0.2–0.8, incidence 0– 20°, 2 altitudes) → ~10,000 samples used to train an XGBoost surrogate driving a Differential Evolution search.
Inputs
Geometry bounds,
flight conditions,
travel bounds
Aerodynamic
Data Generation
Datcom: 15 geometry
vars × 110 flight pts
Initialize DE
Population
Candidate geometry
vectors (p members)
OUTER LOOP — Differential Evolution (per generation, per candidate)
Generate
Mutant Vector
V = X + K(Xbest−X)
+ F(Xb−Xc)
Variable
Crossover
Trial vector;
Cr scaled by rank
Maximum
Crossover
Gene-wise swap
refinement
Selection
Trial vs target;
keep the fitter
constraints checked: wing semi-span = 1500 fixed • body length ≥ tail LE + tail root chord • CD ≥ 0.12
INNER LOOP — Fitness Function
(XGBoost, per flight condition)
Iterate over 110 flight
conditions (Mach, α, Alt)
XGBoost predicts
CL, CD, XCP
Weighted average across
all flight conditions
Fitness = 0.95·F1(CL/CD)
+ 0.05·F2(XCP target)
Traversed all candidates & generation limit?
Output: Configuration with best fitness (optimal geometry)
Extensions: Ensemble XGBoost (5 seeded models, averaged) & MLP Regressor for CN/CM

## Slide 4
4
Results & Discussion, Recommendations
Surrogate Model Accuracy (R²)
Chart: 
| CL | CD | XCP | CN | CM/CD
R² (train) | 0.9994 | 0.9996 | 0.9998 | 0.9978 | 0.9924
R² (test) | 0.9994 | 0.9996 | 0.9451 | 0.8103 | 0.7669
CL, CD (PDF Fig. 5-6) • XCP (Fig. 11, 15 samples) • CN, CM/CD (Fig. 12, 61 samples) — small-sample test spread noted in source
Key Findings
Peak CL/CD improvement ≈ 67% (incidence 3–8°) for the redesigned baseline geometry
Only ~1.7% increase in structural weight (Steel AISI 304) — DRDL-validated against real Datcom runs
DE search evaluated thousands of candidates at near-zero cost vs. repeated CFD/Datcom runs
Specific-point optimization: min-XCP = 9.99, max-CN = 0.54, max-CM/CD = 7.67 (3-variable studies)
RECOMMENDATIONS / SOLUTION
Adopt the constrained XGBoost + Differential Evolution pipeline as the standard design tool. It is “physics-blind” — all physics is encapsulated in the training data — so it extends to any configuration, flight regime or constraint set, limited only by the accuracy of the underlying aerodynamic data model.
R² > 0.99
CL & CD accuracy
~67%
peak CL/CD gain
10,010
training samples
+1.7%
weight change
Discussion: the ML surrogate captured non-linear CL/CD/XCP relationships with low RMSE; DE showed stable, monotonic convergence across generations, confirming a reliable, low-cost alternative to conventional CFD-based aerodynamic design.

## Slide 5
5
Conclusion & Future Scope
CONCLUSION
A methodology for optimal design of a complex aerospace vehicle configuration (multiple components) was developed
The design is comprehensive — it optimizes across the complete flight envelope in one go, with user-settable priority weights per flight condition and hard/soft geometric constraints
Differential Evolution (outer loop) coupled with an XGBoost fitness function (inner loop) reliably drives the search toward high-performance, physically valid configurations
The framework is “physics-blind” by design — the physics lives entirely in the training data — so it generalizes to other configurations and flight regimes
FUTURE SCOPE / PROPOSED PLANS
Multi-objective optimization — jointly maximize CN and CM/CD (noted in the source as future work, outside this project's scope)
Physics-Informed Machine Learning — merge the Aerodynamic Data Generation, Fitness Function and Evolutionary Design phases into one unified system
Extend surrogate coverage with the docx's Ensemble XGBoost and MLP (CN, CM) models for broader coefficient prediction
Bottom line:
ML-driven surrogate modelling combined with evolutionary optimization is a reliable, fast and computationally efficient alternative to conventional simulation-based aerodynamic design.